## Slide 1
OpenRiverCam in Indonesia
What the pilot taught us, and the path forward Response to the PMI / IPB / BHLK meeting, Sukabumi, 21 August 2026
Palang Merah Indonesia · Institut Pertanian Bogor · Balai Hidrologi dan Lingkungan Keairan · American Red Cross
2026-08-31 · Draft for internal review — not yet circulated

## Slide 2: The pilot, and what we think comes next
The pilot has been a good experience. A station in the water, four months of behaviour to learn from, and a working relationship between PMI, IPB and BHLK that did not exist before.
Our recommendation is that the next step is yours.
  Not because the partnership has run its course, but because of what the pilot produced: knowledge, not a body of measurements.
  Knowledge is worth more to you as an input to your own approach than as a set of parts to copy.
We would rather help you start your own design than hand you ours to maintain.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
2 / 21

## Slide 3: What this briefing covers, and what it leaves to you
The technology only: the station as built, what four months in the field revealed, and what we would change before more units are constructed.
Not in scope: what the data is fit to support, or what accuracy any application requires.
  Those judgements belong with IPB, BHLK and their federal partners.
  Measurement requirements shown here are recorded from you, not proposed by us.
Written to give an accurate basis for your decision rather than an encouraging one.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
3 / 21

## Slide 4: Three offers were made on 21 August. We welcome all three.
Build one to three stations as a pilot.
  Supported. What follows is what we would change first.
Provide server capacity for the data.
  Well matched to the pilot, and holding the data in Indonesia carries a clear benefit.
Move the present site to open ground.
  Supported, and the field record adds independent evidence for it.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
4 / 21

## Slide 5: Why a low-cost station is worth studying
A river gauge is only useful if there are enough of them. How many an agency can afford decides how much of a catchment it can observe.
This station: USD 1,340 in materials — electronics and enclosure only. Sukabumi already had its panel and battery, so a new solar site would add an array. A mains site would not.
Lowest-cost automatic water-level station on the government e-catalogue: about USD 3,600 before VAT, measuring stage only.
  Not like for like — that is a supported commercial instrument, this is a pilot-stage assembly.
At this price a basin authority can consider a network where it might otherwise consider a single gauge. That possibility is the whole of the argument.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
5 / 21

## Slide 6: What is being offered for study
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
6 / 21

## Slide 7: Built from commodity parts, so it can be repaired locally
The parts for one station, before assembly.
The same parts wired onto the plate, under bench power.
No soldering, no fabrication, nothing single-source.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
7 / 21

## Slide 8: The evidence is thin, and we ask you to treat it as thin
One station, on one river, watched across part of one season — 16 April to 28 August 2026.
A second station was built but never installed.
What the deployment has produced so far is knowledge about the design, not a body of measurements.
It is a volunteer pilot and should be read as one.
  Never built to production standards of availability or record continuity. Measuring it against an industrial instrument would be the wrong test, and unfair to the people who kept it running.
  The useful question is narrower: what does this design make hard, and what should be built differently.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
8 / 21

## Slide 9: Three design gaps, and what we would build instead
The station cannot report its own condition. When it stopped, it stopped quietly.
  Instead: report state on every waking, and make any mode that suppresses data expire on its own and raise an alert. R4, R5.
Nothing reconciles what was recorded against what arrived.
  Instead: compare the station's record against the server's on a schedule. Small piece of software; should have been in version one. R7.
Water level is read from the image, and daylight defeats it.
  Instead: an independent water-level reference, so the measurement does not rest on one optical method succeeding. R1.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
9 / 21

## Slide 10: The station measures water level reliably only at night
The two peaks and the early-afternoon dip are the pattern a sun-angle effect produces.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
10 / 21

## Slide 11: Eleven things we would do differently
Offered as input to your design, not as corrections to ours. We would not expect them adopted as a set.
Let the station account for itself — R4, R5, R6, R7.
  Nothing here is difficult or costly. The setting behind nine of the thirteen interruptions was readable remotely the whole time, and no software asked.
Make the measurement trustworthy — R1, R2.
  An independent water-level reference, and survey planned as professional work from the start. We learned that the hard way; IPB's total-station survey is what the station runs on today.
Make the units buildable and maintainable in Indonesia — R3, R8, R9, R10, R11.
  You will buy under Indonesian procurement rules, so substitution is the expected case rather than a risk to be managed.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
11 / 21

## Slide 12: R1–R6
# | Change | What it buys | Cost
R1 | Fit an independent water-level reference | Measurement through the day | A sensor, or a staff gauge in view
R2 | Commission a professional survey first | The one input processing cannot recover | Rp 5–15 million per site
R3 | Specify interfaces, not part numbers | Local procurement without referring back to us | Documentation only
R4 | Health reporting and mode alarms as requirements | The station reports its own condition | Negligible
R5 | Station sends diagnostics; no login required | Support inside a short waking period | Small
R6 | Record voltage and current together | Separates a failing battery from a heavy load | A sensing module
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
12 / 21

## Slide 13: R7–R11
# | Change | What it buys | Cost
R7 | Compare recorded against received, automatically | Loss is noticed, not discovered later | Negligible
R8 | Put the computer indoors | Removes it from heat, humidity, dust and travel | Designed, not yet field tested
R9 | Budget per station; check the interface before buying | A network that stays affordable | Screening effort
R10 | Use the computer's own clock where the site allows | One less board to fail | Saves about USD 50 per station
R11 | Build on mains and leave it running, where continuous reporting is wanted | Removes most of the gaps above | No solar array to buy; constrains siting
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
13 / 21

## Slide 14: R8 — the least proven change, and possibly the most useful
Designed and not yet field tested — the pilot's first experiment, not a proven alternative.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
14 / 21

## Slide 15: One lesson about method
The budget was applied part by part: the cheapest item meeting each requirement.
It prices each part against its specification sheet, not against what that part's limits cost the rest of the system.
The camera meets every line of its specification, and still costs a fifth of the video quality and 30–60 s of battery on every waking.
Its light fires whenever it starts and cannot be turned off — 48 flashes a day at the present site.
Capable hardware, running a reseller's version of the manufacturer's software.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
15 / 21

## Slide 16: Building and looking after the units in Indonesia
The design was made to be built by people who are not electronics specialists, with tools they already own.
That intent only becomes real if the parts can be bought locally and the documentation supports substitution — R3.
Spares held at the local PMI chapter turn a failure into a part swap rather than a shipment.
Where the field unit is a standard security camera, support falls within a supply chain that already exists across Indonesia.
We would rather help build the capacity to maintain these stations than remain the place they are sent when they break.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
16 / 21

## Slide 17: Hosting the data in Indonesia
BHLK's offer suits the pilot, and holding the data in Indonesia carries a clear benefit for a government-partnered deployment.
Two constraints to design for rather than discover:
  The video store and the database must share one filesystem. Plan storage as a single volume.
  Server and station software versions are tied together, and a remote station cannot be upgraded on demand.
We would suggest running both instances in parallel until the new one has completed a full operating cycle, including an upgrade.
Worth agreeing in writing: where the authoritative copy sits, who administers it, who has access, and the retention policy.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
17 / 21

## Slide 18: Choosing the sites
An open site helps with three problems at once: satellite positioning, the sun-water-camera angle, and the view across the section.
A move costs a fresh survey and a fresh calibration, not only a relocation. The survey is the expensive part.
Site permission should be settled before a unit is built for a particular site.
  A complete station was built and tested for an intended Jakarta site. Permission fell through during the April visit.
That station is still available. We suggest it serves best as a study and test unit.
  Open it, trace it, power it up, take it apart — and install it somewhere convenient and local if that is useful, so it can be exercised against real water.
  Not as an operational station with expectations of availability and consistent data. It carries the design this briefing recommends changing.
We would not build to a site again before you tell us the permission is in place.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
18 / 21

## Slide 19: Working together
BHLK — data processing, conformance with standards, and the route to acceptance within PUPR data systems. Offers server capacity.
IPB — design, calibration methodology, training material, and the development path for future sensor types.
PMI — user of the information, and the operational side: installation, maintenance, siting, response, and spares.
Offered for your consideration: write the split into the collaboration agreement so it survives staff changes, and keep a light joint forum for what does not sort into one role.
The commitments this implies for PMI have not been discussed with PMI National Headquarters.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
19 / 21

## Slide 20: Questions for consideration
Who should hold the Jakarta station as a study and test unit? It was to transfer to IPB for deployment. Whether IPB or BHLK is better placed to hold it is for the two of you.
Can a staff gauge be read from the camera image accurately enough? If it can, R1 needs no separate sensor.
Two of the thirteen interruptions remain unexplained.
Does the recovery-voltage threshold bound how long an interruption lasts, or hold the station off?
How does the velocity measurement perform across the surface conditions the pilot sites present?
Absolute discharge accuracy at Sukabumi, unresolved pending the survey.
We expect your work to change some of what is written here. That is the point of handing it over rather than handing it down.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
20 / 21

## Slide 21: What we can offer from here
We are not proposing to build your stations.
What we can offer is the record: this briefing and its report, the appendix, the operator and assembly documentation in English and Bahasa Indonesia, the software, and the built station at Wisma PMI to take apart.
Beyond that, whatever is useful — reviewing a design, answering a question about something that surprised us, looking at data that does not behave.
Sukabumi will keep running, and we will keep reporting what it does, including the parts that go wrong.
The pilot found the problems while they were still cheap, and it introduced three organisations to one another. The next station in this story should be one you designed.
ORC Indonesia — PMI · IPB · BHLK · American Red Cross
21 / 21